## Slide 1: Using beam simulations to model mutual coupling coefficients in the MWA Phase II compact array
Katherine Elder, PhD Student
Dr. Daniel C. Jacobs

## Slide 2: Why haven’t we detected the EoR yet?
21 cm signal very faint
Limited by instrumentation uncertainty
  Beam pattern is a main uncertainty
We need to understand our instruments extremely well
https://github.com/EoRImaging/eor_limits

## Slide 3: Murchison Widefield Array (MWA)
Phase II
Two Hexagonal sub-arrays
  36 tiles each
More sensitive to 21 cm signal
  Short, redundant baselines
https://www.mwatelescope.org/

## Slide 4: Common Mode Signal
Kolopanis et al (2023) found a strong common mode signal in Phase II data
This introduces a statistically significant bias
Short baselines are the most sensitive to EoR
  Previously all short baselines were flagged
  ~50% of short baselines still flagged
0
Delay [ns]
Time [LST]

## Slide 5: Sources of excess correlation
Re-radiation is one part of mutual coupling
How much does mutual coupling affect the visibilities?

## Slide 6: Mutual Coupling Models
Numerical EM simulator (FEKO)
  Detailed model of antenna
  Models multiple paths for excess correlation
    Direct Re-radiation
    Re-radiation Reflection
  Time consuming
  Computationally expensive
Re-radiation model
  Simplified model
    Only need simulation of one antenna
  Fast and easy
  Easy to scale up
  Only models single path for excess correlation
    Direct Re-radiation

## Slide 7
Re-radiation model:
  Direct path
Numerical EM model:
  Direct path
  Reflections

## Slide 8: Choosing the baselines
Kolopanis et al. (2023) looked at three baselines
  14m, 24m, 28m
  Shortest
  Most redundant
  Most sensitive to 21 cm signal

## Slide 9: Multipath Re-radiation model
FEKO modeling software
Model details same as the 2016 FEE beam model
Model has an LNA and a voltage source
Array is N-S polarized
Sokolowski et al. (2017)

## Slide 10: Multipath Re-radiation model
14 m baselines
24 m baselines

## Slide 12: Single path Re-radiation model
Rath et al. (2024) (arXiv:2406.08549) define the visibility equation with mutual coupling as:
Where is the original visibility, is the mutual coupling coefficient, and is the adjusted visibility

## Slide 13: Coupling coefficient
is the wavelength, is the reflection coefficient, is the beam area, is the frequency, is the baseline length, and J() is the far field radiation pattern
, , and J() are calculated in FEKO for a single tile

## Slide 14: Single path Re-radiation model

## Slide 16: Why does any of this matter???

## Slide 17: How much does mutual coupling affect the visibilities?

## Slide 18: DO WE NEED TO BE WORRIED ABOUT IT??

## Slide 19: Total mutual coupling approximation
We approximate to be identical for all baselines and ij as interchangeable, we can sum over for every baseline

## Slide 20: Worst Case Scenario
Using the limits reported by Trott et al. (2020), we approximate a limit of ~ -20 dB for the visibilities
The sum must be lower than -20 dB

## Slide 21: Single Path Re-radiation model for all baselines

## Slide 25: Summary and Conclusions
We need to know how much mutual coupling affects the visibilities
The models show:
  Adding more tiles increases mutual coupling
  A rough approximation shows mutual coupling is near EoR power spectrum limits only at high frequencies
Open questions:
  Why is there a >20 dB difference between models?
  Is -20 dB the actual EoR power spectrum limit?
Name: Katherine Elder
Email: kat.elder@asu.edu

## Slide 26: Extra Slides

## Slide 28: Single Tile 3D Beam Pattern

## Slide 29: Single Tile 3D Beam Pattern